%
the p5
glove controller
audio processing
with free sound
software
p5 glove controller :: jason plumb :: http://noisybox.net/

---
not a nintendo powerglove
but similar
IR instead of
ultrasound
5 versus 4 fingers
improved flex resolution
pitch, yaw, and roll
usb

---
essential reality p5 glove </background>
siggraph 2001
initial retail ~ $100-$150
targeted at gamers
tanked
company gone(??)

---
essential reality p5 glove
[[[[[object]]
5 finger bend
3D position
(X,Y,Z)
roll/pitch/yaw
4 buttons
usb powered

---
[[[[[object]]
uses IR
multiple emitters
multiple (embedded) receivers
math

---
s o ftw a r e
spotty ER Linux support
community grown drivers and tools!
(better than the vendor's./././duh)
jason mcmullan wrote libp5glove
[for libusb]
yahoo group (but lin/win ratio is low)
http://www.simulus.org/p5glove/

---
s o ftw a r e
pure-data (pd) ::::: for great victory
feed::
software synthesizers
internal/external midi devices
other pd patches
...but how to we get from the driver to [pd]?

---
s o ftw a r e^^
p5osc
dumpOSC
OSC/UDP
libp5glove
p5glove.pd
libusb
pure-data (pd)
usb support
kernel
audio
glove hardware
???
MIDI

---
so f twa re
Q:....well that's a lot of boxes...why not just write a [pd] external, silly?
A: libusb doesn't support nonblocking bulk reads...yet
A: libOSC provides nice network separation

---
d e m o s
basic synthesis in pd
filter parameter control
sound fonts

---
IMPROVEMENTS?
8/16/24 byte alignment patch
line of sight recovery
startup issues
inappropriate error messages
kernel conflicts with usbfs[?]
calibration requires w*ndows?
option to use unix socket for OSC

---
fin
Q & A